## Slide 1: User Identification based on Movement
CS6330 Final Project
Dan Olson
Rich Lukas
Robert (George) Burkhardt

## Slide 2: User Identification based on Movement
Problem Statement
The Goal of this project was to collect time series data from an IMU, and use it to identify individuals and activities
  Movement is highly individualized and unique to each person
    Gait is the cyclic movement of the body during locomotion
  Gait can be broken down into the Stance phase and Swing phase
    Stance Phase Stance Phase
      Heel Strike Acceleration Phase
      Foot Loading Mid-Swing
      Midstance shift Deceleration Phase
      Heel-off
      Toe-of
  Typical methods of analysis consist of stop motion photography, pressure sensors, and accelerometers strapped to the body.

## Slide 3: User Identification based on Movement
Methodology
Data Collection
  Three test subjects were outfitted with a 6 axis IMU (inertial measurement unit), which recorded angular velocity and acceleration
    Data was collected at 500 Hz and then down sampled to 100 Hz
    The sensor was mounted at the hip
  The recorded activities included
    Walking at a measured pace
    Running
    Stair climbing/descending
    Treadmill
    Sitting
    Jumping
    Standing
  Data was generated (as opposed to using primary & secondary sets)

## Slide 4: Exploratory Data Analysis

## Slide 5: Uniqueness of Gait
Dan Olson

## Slide 6: Uniqueness of Gait
Rich Lukas

## Slide 7: Uniqueness of Gait
George Burkhardt

## Slide 8: Uniqueness of Gait Compared
Visualization

## Slide 9: Forces in 3-space
Visualization of Motion

## Slide 10: Model the First
Identifying Individuals

## Slide 11: Identifying Individuals
Baseline Model
Identify Individuals
  Our baseline model was a Logistic Regression Classifier. We tested a velocity only and acceleration only version
Angular Velocity Only
Angular Acceleration Only

## Slide 12: Identifying Individuals
Model Iteration
Improved Model
  We next tried a model using both angular velocity and acceleration, then applied a low pass filter to smooth the data. The results were slightly better

## Slide 13: Identifying Individuals
Linear Models
Best Logistic Model
  After looking at the outliers, we added an additional EWMA (exponentially weighted moving average) filter with a half-life of 100ms to add more trend data to the model

## Slide 14: Identifying Individuals
Linear and Non-Linear Models
Exploring Other Classifier Types
  The KNN model did the best, outperforming all other models. All models were built on stratified Train Test data and compared using a separate validation dataset
  However, the KNN might not translate well to embedded devices
Model | Balanced Accuracy
Logistic Regression | 0.9688
SVM | 0.9437
Random Forrest | 0.9703
Decision Tree | 0.9611
KNN | 0.9961
MLP | 0.9818

## Slide 15: Identifying Individuals
KNN Results
KNN Results

## Slide 16: Identifying Individuals
KNN Residuals
KNN Residuals

## Slide 17: Identifying Individuals
Model Reduction
Reduced Features
  To reduce the feature set for user identification, a CART (classification and regression tree) analysis was performed on the Decision Tree Classifier (which had results like the KNN)
  The CART analysis shows that the exponentially weighted filtered terms have the greatest significance
Features | Score
gFyE | 0.638
gFxE | 0.212
wzE | 0.076
gFzE | 0.023
wx | 0.014
… | …
Reduced to gFxE, gFyE, and gFzE

## Slide 18: Model the Second
Identifying Activities

## Slide 19: Identifying Activities
Principal Component Analysis
Feature Engineering
  Time series data on a variety of activities was collected and labeled. The same feature set as before was used to build classifier models. To help visualize the data a partial correlation analysis was taken to reduce the feature set.

## Slide 20: Identifying Activities
Baseline Model
Identify Activities
  Following the same procedure as before, we tested a logistic regression classifier model using angular velocity and acceleration. Adding additional features did not significantly improve the results.
Baseline model (angular velocity and acceleration)
Full Model using all 18 features
S (Sitting) C (Climbing) W (Walking)

## Slide 21: Identifying Activities
Linear and Non-Linear Models
Exploring Other Classifier Types
  The Logistic Model did not seem promising. To resolve this other models were tested
  The KNN model did the best, outperforming all other models. All models were built on stratified train-test data, and compared using a separate validation dataset
Model | Balanced Accuracy
Logistic Regression | 0.6857
SVM | 0.6599
Random Forrest | 0.9155
Decision Tree | 0.981
KNN | 0.9943
MLP | 0.9128

## Slide 22: Identifying Activities
KNN Results
KNN Results

## Slide 23: Identifying Activities
KNN Residuals
KNN Residuals

## Slide 24: Identifying Individuals
Model Reduction
Reduced Features
  A KNN model for activity identification was built using only exponentially filtered term based on the CART analysis. The results were nearly identical to the full model, showing the model reduction is valid.
Features | Score
gFxE | 0.212
gFzE | 0.201
gFyE | 0.168
wxE | 0.08
wyE | 0.044
wzE | 0.04
… | …
Reduced to gFxE, gFyE, gFzE, wxE, wyE, and wzE

## Slide 25: Conclusion
Did we succeed?

## Slide 26: Identifying Individuals
Linear and Non-Linear Models
Success – but more to do!
  Based on our findings, these explorations could be extended further
    Identify Speed/Length of Stride
    Abnormal locomotion
    Handedness
    Stance
    Tool Positioning
  In principle we can build a power tool that identifies its operator using gait biometrics, rather than a user id. This also suggests that a tool could be customized based on how a user is holding the tool (e.g. righty vs lefty)
  Reasonable model improvements could involve measuring IMU at several points on the body and using stride length as an additional feature

## Slide 27: About Us
Before we go…

## Slide 28: About Us
ML-ers Extraordinaire
Rich Lukas
  Mgr EE
  ML Team, FEI
  Big Takeaways
    A great deal of information is buried in IMU data. We can infer a great deal about a work site and user behavior.
    Greater confidence in our ability to measure/model our environment beyond simply tool performance.
    Ability to manipulate data in Python and create sophisticated analysis.

## Slide 29: About Us
ML-ers Extraordinaire
Dan Olson
  TBD
  Big Takeaways
    TBD

## Slide 30: Question and Answers