## Slide 1: CS 6330 Final Project
Human Gait Analysis
Dan Olson
Rich Lukas
Robert Burkhardt

## Slide 2: CS 6330 Final Project
Problem Statement
The Goal of this project was to collect time series data from an IMU, and use it to identify individuals and activities
  Gait is the cyclic movement of the body during locomotion
  Gait can be broken down into the Stance phase and Swing phase
    Stance Phase Stance Phase
      Heel Strike Acceleration Phase
      Foot Loading Mid-Swing
      Midstance shift Deceleration Phase
      Heel-off
      Toe-off
  Movement is highly individualized and unique to each person
  Typical tools consist of stop motion photography, pressure sensors, and accelerometers strapped to the body.

## Slide 3: CS 6330 Final Project
Methodology
Data Collection
  Three test subjects were outfitted with a 6 axis IMU, which recorded angular velocity and acceleration
    Data was collected at 500 hz and then down sampled to 100 hz
    The sensor was mounted at the hip
  The recorded activities included
    Walking at a measured pace
    Running
    Stair climbing/descending
    Treadmill
    Sitting
    Jumping
    Standing

## Slide 4: CS 6330 Final Project
Visualization
Visualization of IMU Data Walking at 1 step per second

## Slide 6: Uniqueness of Gait
Visualization

## Slide 7: Uniqueness of Gait
Visualization

## Slide 8: Forces in 3-space
Visualization

## Slide 9: Forces in 3-space
Identify Individuals
An Ensemble of walking gait data was created The data was stratified into
Training, Test data, and Validation sets. The Training data consisted of
18 features
Instantaneous Angular velocity and acceleration
Low pass filtered versions of each input
EWMA of each input, with a half life of 100 ms