## Slide 1: CS 6330 Final Project
User Identification based on Movement
Dan Olson
Rich Lukas
Robert Burkhardt

## Slide 2: CS 6330 Final Project
Problem Statement
The Goal of this project was to collect time series data from an IMU, and use it to identify individuals and activities
  Gait is the cyclic movement of the body during locomotion
  Gait can be broken down into the Stance phase and Swing phase
    Stance Phase Stance Phase
      Heel Strike Acceleration Phase
      Foot Loading Mid-Swing
      Midstance shift Deceleration Phase
      Heel-off
      Toe-off
  Movement is highly individualized and unique to each person
  Typical tools consist of stop motion photography, pressure sensors, and accelerometers strapped to the body.

## Slide 3: CS 6330 Final Project
Methodology
Data Collection
  Three test subjects were outfitted with a 6 axis IMU, which recorded angular velocity and acceleration
    Data was collected at 500 hz and then down sampled to 100 hz
    The sensor was mounted at the hip
  The recorded activities included
    Walking at a measured pace
    Running
    Stair climbing/descending
    Treadmill
    Sitting
    Jumping
    Standing

## Slide 4: CS 6330 Final Project
Visualization
Visualization of IMU Data Walking at 1 step per second

## Slide 5: Uniqueness of Gait
Visualization

## Slide 6: Uniqueness of Gait
Visualization

## Slide 7: Forces in 3-space
Visualization

## Slide 8: Forces in 3-space
Visualization

## Slide 9: Forces in 3-space
Identify Individuals
Identify Individuals
Our initial model was a Logistic Regression Classifier.
Angular Velocity Only
Angular Acceleration Only

## Slide 10: Forces in 3-space
Identify Individuals
We then built a model using both angular velocity and acceleration, and applied
a low pass filter to smooth the data

## Slide 11: Forces in 3-space
Identify Individuals
After looking at the outliers, we added an addition EWMA filter with a half
Life of 100 ms to add more trend data to the model

## Slide 12: Forces in 3-space
Best Model for User Identification
Multiple Classifier models were developed, including
  Logistic Regression Support Vector Machine
  Random Forest Decision Tree
  K Nearest Neighbors Multi-layer Perceptron Classifier
The KNN model did the best, outperforming all other models. All models were built on stratified Train Test data and compared using a separate Validation dataset.

## Slide 13: Forces in 3-space
Best Model Results User Identification
Six Different Classifier Models were evaluated, to identify a unique individual. Overall, the best classifier in repeated testing was a model based on K Nearest Neighbors.

## Slide 14: Forces in 3-space
Identify Activity
Part Two: Identify Activity
Time series data on a variety of activities was collected and labeled. The same feature set as before was used to build classifier models. To help visualize the data a partial correlation analysis was taken to reduce the feature set.
Visually it can be seen
that the data clusters
are heavily overlapped.

## Slide 15: Forces in 3-space
Baseline Activity Detection
Following the same procedure as before, we tested a Logistic regression
Classifier model using angular velocity and acceleration. Adding filters did not
Significantly improve the results.
Model using only angular velocity and acceleration
Model using angular velocity, acceleration, and all filters
S (Sitting) C (Climbing) W (Walking

## Slide 16: Forces in 3-space
Best Model for Activity Identification
To improve the results other models were tested
Multiple Classifier models were developed, including
  Logistic Regression Support Vector Machine
  Random Forest Decision Tree
  K Nearest Neighbors Multi-layer Perceptron Classifier
The KNN model did the best, outperforming all other models. All models were built on stratified
Train Test data, and compared
using a separate Validation
dataset.

## Slide 17: Forces in 3-space
Reduction
Reduced Feature Set
To reduce the feature set for user identification, a CART analysis was performed on the Decision Tree Classifier (which had results like the KNN)
From the CART analysis the top features ranked are
gFyE | Score: 0.638
gFxE | Score: 0.212
wzE | Score: 0.076
gFzE | Score: 0.023
wx | Score: 0.014
wz | Score: 0.011
wyE | Score: 0.007
wy | Score: 0.006
wxm1 | Score: 0.003
gFzm1 | Score: 0.002

## Slide 18: Forces in 3-space
Reduction
Reduced Feature Set
A KNN model was built using only gFxE, gFyE, gFzE, based on the CART analysis.

## Slide 19: Forces in 3-space
Summary
We met the ask of identifying activity, and identifying individuals based on their gait.
Based on our findings, these explorations could be extended further
Identify Speed/Length of Stride
Abnormal locomotion
Handedness
In theory we can build a power tool that can identify its operator using gait biometrics, rather than a user id. This also suggests that a tool could be customized based on how a user is holding the tool (righty vs lefty etc)
Reasonable model improvements could involve measuring IMU at several points on the body, and using stride length as an additional feature.